## Slide 1
HACKATHON PROTOTYPE
EMG Progressive
Overload Coach
Measures muscle activity and movement to estimate reps in reserve—and turn effort into a clear training decision.
EMG
+
PHONE IMU
Notes: Introduce the project in one sentence: most trackers count what happened; this coach estimates how hard the muscle worked.
[Sources]
- User-provided prototype data and project specifications.

## Slide 2
The same workout can represent very different effort
2
Traditional tracking sees only the external work.
What trackers see
15 lb
10 repetitions
Same exercise
What the coach adds
Muscle activation
Movement quality
Estimated RIR
Goal: recommend whether to continue, stop, maintain the load, or progress it next time.
Notes: Use a simple example: two people can complete the same weight and reps while having very different reps remaining.
[Sources]
- User-provided prototype data and project specifications.

## Slide 3
Two sensors capture internal effort and external performance
3
Biceps EMG
Backyard Brains WAV
→ EMG RMS + change
Phone IMU
Gyroscope + accelerometer
→ reps, speed, jerk
→
Per-rep features
• EMG RMS change
• Peak angular velocity
• Rep duration
• Dynamic acceleration
• Movement jerk
→
Personalized output
Estimated RIR
Training status
Next-step recommendation
Separate recording clocks are aligned automatically before features are calculated.
Notes: Explain that EMG and phone recordings can start at different times. The software aligns their activity patterns, detects working reps, and rejects synchronization or partial movements.
[Sources]
- User-provided prototype data and project specifications.

## Slide 4
RIR turns sensor data into an actionable coaching signal
4
RIR = how many additional good-form repetitions the person could still complete.
MORE REPS
4+ RIR
Effort is still low.
Continue the set.
TARGET ZONE
1–3 RIR
Desired challenge.
Maintain the load.
STOP SET
0–1 RIR
Near failure.
End the set safely.
At the top of the target rep range with substantial RIR remaining → increase weight next session.
Notes: Walk left to right. The system separates the immediate set decision from the next-workout load decision.
[Sources]
- User-provided prototype data and project specifications.

## Slide 5
The first personalized prototype spans easy effort to failure
5
Chart: Completed repetitions
| Easy 5 RIR | Moderate 3 RIR | Failure 0 RIR
Completed reps | 4 | 7 | 13
24
labeled repetitions
across 3 sets
±1.72
RIR group-validation
mean error
Promising first pass—not yet independent validation or a medical device.
Notes: Present these as prototype results. The ±1.72 RIR value comes from leave-one-set-out testing on the three calibration sets.
[Sources]
- User-provided Subject 1 calibration trials: 15 lb, 4 reps at 5 RIR; 7 reps at 3 RIR; 13 reps at 0 RIR.

## Slide 6
NEXT STEP
Validate first.
Then coach live.
Run a new 15-lb set stopped at 1–2 RIR without retraining the model. Compare predicted vs. reported RIR, then connect the validated output to the dashboard.
The experience
Rep 8
Estimated RIR: 2
TARGET ZONE
Maintain 15 lb
Measure effort—not just repetitions.
6
Notes: Close by showing the desired real-time user experience. The immediate validation goal is prediction within approximately ±2 RIR and correct identification of the near-failure zone.
[Sources]
- User-provided prototype data and project specifications.